## Slide 1
Jose E. Schutt-Aine
Electrical & Computer Engineering
University of Illinois
jesa@Illinois.edu
ECE 453
Wireless Communication Systems
Oscillators

## Slide 2
Feedback – Basic Concept

## Slide 3
  The closed-loop transfer function is a function of frequency
  The manner in which the loop gain varies with frequency determines the stability or instability of the feedback amplifier
  The frequency at which the phase of the transfer function is equal to 180o will be unstable if the magnitude is greater than unity
Feedback and Frequency Dependence

## Slide 4
Feedback and Stability
When loop gain A(jw)b(jw) has 180o phase, we have positive feedback

## Slide 5
Nyquist Plot
Radial distance is |Ab|
Angle is phase of f
Intersects negative real axis at w180

## Slide 6
Stability and Pole Location

## Slide 7
Oscillator
Closed-Loop Transfer function:
Barkhausen’s criteria for oscillation:
  
  
= oscillation-frequency.

## Slide 8
Oscillator Topologies
Common-base topology is usually preferred because
  Feedback within transistor is minimized (low Miller)
  External feedback is dominant
  Current gain has little phase shift and is constant with f
Oscillator built around 2 major requirements:
  Oscillation frequency fo
  Power Po that must be delivered to a load
Other criteria
  Efficiency
  Spectral purity
  Frequency stability

## Slide 9
BJT – High-Frequency Model

## Slide 10
Common-Collector Colpitts
Minimize circuit dependence on transistor internal parameters
Choose

## Slide 11
For Oscillation, we want Zleft = -Zright
Incremental Model

## Slide 12
Oscillation Criteria
Term in w-4 can be neglected. This gives
Gives transconductance gms to set net resistance to zero
Condition gives

## Slide 13
Oscillation Conditions
If gm << wC1b and assuming that b is large,
In terms of the inductor quality factor QL
gms is the transconductance needed to support steady-state oscillations

## Slide 14
CC-Colpitts - Observation
To implement tunable oscillator
  Use variable capacitor in parallel or is series with inductor
To extract power from oscillator
  Place resistance in shunt with inductor
  Account for loading effect in analysis and design
  Oscillation amplitude builds up and vbe increases
  Transistor moves out of linear range and operation becomes nonlinear. Transconductance decreases.
  When transconductance reaches gms, steady state operation is achieved.

## Slide 15
Common-Base Colpitts
  Cf : tuning capacitor
  C1 & C2: feedback ratio
  RFC: RF choke to prevent power dissipation in RE
  RP is equivalent resistance of coil Lt.
  DEFINITIONS

## Slide 16
Setting the determinant to zero provides the criterion for the onset of oscillation.
CB-Colpitts - Incremental Model

## Slide 17
CB-Colpitts - Oscillation Conditions
Setting the determinant to zero gives.
Defining
and
we get a complex conjugate pair of roots. This leads to 2 equations for real and imaginary parts that must be equal to zero separately

## Slide 18
CB-Colpitts - Oscillation Conditions
From the equation for the imaginary part, we get
or
First term should predominate

## Slide 19
CB-Colpitts - Oscillation Conditions
In that case
which leads to
Circuit oscillates at frequency determined by Lt and equivalent capacitance.

## Slide 20
CB-Colpitts - Oscillation Conditions
The solution of the real part using w = wo gives
For oscillations to start, a of the transistor should be greater than amin.

## Slide 21
Crystal Oscillator
Quartz exhibits piezoelectric effect
  Reciprocal relationship between mechanical deformation and appearance of electrical potential
  Deforming crystal produces voltage
  Applying voltage produces deformation
When applied voltage is sinusoidal
  Mechanical oscillations that exhibit resonances at multiple frequencies
  Extremely high Q that can reach 105 and 106
  Do not work above 250 MHz

## Slide 22
Crystal Resonator - Circuit Model
Rq, Lq and Cq describe mechanical resonance behavior C0 is capacitance due to external contacting
- Lq ,Cq, Rq describe mechanical resonance
- C0 is due to external contacting

## Slide 23
Crystal Resonance Frequencies
Admittance from terminals is
Resonance condition is expressed by

## Slide 24
Crystal Resonance Frequencies
Series resonance frequency
Parallel resonance frequency
where

## Slide 25
Crystal is characterized by Lq = 0.1H, Rq = 25W, Cq = 0.3pF, and C0 = 1 pF. Find series and parallel resonance frequencies and compare them against the susceptance formula.
Crystal Oscillator - Example

## Slide 26
Voltage Controlled Oscillator
Varactor diode exhibits large change in capacitance in response to an applied bias voltage
Varactor diode

## Slide 27
Voltage Controlled Oscillator

## Slide 28
Voltage Controlled Oscillator
Finding input impedance
Re-write as (assuming h11>>XC1 and b+1 ~ b )
Using gm = b/h11
Negative resistance

## Slide 29
Resonance frequency follows from condition:
which gives
and
VCO – Resonance Frequency
Combined resistance of varactor diode must be equal to or less than |RIN| to create sustained oscillations
where

## Slide 30
Simulation - Colpitts Oscillator

## Slide 31
Simulation - Colpitts Oscillator

## Slide 32
Simulation - Pierce Oscillator

## Slide 33
Simulation - Pierce Oscillator

## Slide 34
Simulation - Ring Oscillator